## Slide 1: COASTAL 101 Jefferson Parish Coastal Restoration

## Slide 2: WHAT WE DO
Steward restoration projects
Educate our parish on coastal issues
Issue permits for construction, development, and production activities
Coastal Funding Management & Development

## Slide 3: TODAY’S QUESTIONS
What can we do?
How did the delta form?
What impact did levees have?
Why is Jefferson’s coast important?

## Slide 4: PROBLEM TO SOLVE
COASTAL LAND LOSS IN LOUISIANA

## Slide 5: HISTORIC LAND LOSS
1960
2017
Land Loss in 57 years
30%
Coastal Overview
Notes: Land loss is a gradual process, but it adds up. Between 1960 and 2017, Jefferson parish lost 30% of its land.

## Slide 6: FUTURE LAND LOSS: NO PLAN
WITHOUT PLAN
2067
112
42%
in 50 years
SQUARE MILES
or
Equivalent to Boston falling into the Atlantic
Coastal Overview
Notes: Without human action, we will lose an estimated additional 112 square miles by 2067 – that’s like the entire city of Boston falling away.

## Slide 7: FUTURE WITH PLAN
gained or maintained with 2017 COASTAL PLAN
SQUARE MILES
89
WITH PLAN
2067
Coastal Overview
Notes: With action, we estimate gaining or maintaining 89 of those miles over the next few decades.

## Slide 8: WHY IS JEFFERSON’S COAST IMPORTANT?
FISHERIES
RECREATION
WILDLIFE
JOBS AND INDUSTRY
COMMUNITIES AND CULTURE
CRITICAL ECOSYSTEM
Coastal Overview
Notes: Jefferson Parish’s coast is important for many reasons. It serves as habitat to fish, birds, and wildlife, and provides jobs and natural resources to the state.
We have communities like Jean Lafitte and Grand Isle, where the coast is an important part of life. Plus, you can’t have a fish fry without the fish.

## Slide 9: WHY IS JEFFERSON’S COAST IMPORTANT?
STORM PROTECTION:
IT’S OUR FIRST LINE OF DEFENSE
Coastal Overview
Notes: One thing you might not think about is that coastal areas are our first line of defense against hurricanes and other storms. Here you can see the multiple lines of defense that protect our communities against storm surge. Barrier islands, marshes, ridges – these natural features keep us safe.
We’ll get into some specifics later.

## Slide 10: COASTAL FORMATION
SEDIMENT
COASTAL PLAIN
Image credit: NASA
GLACIER MELT
Coastal Overview
Notes: Let’s back up a bit, and talk about how Louisiana formed. The Mississippi carried water and sediment down to the coast. Over time, this sediment built up and formed land. The river changed course many times, building up the Mississippi Delta as we know it.

## Slide 11: DELTA LOBE FORMATION
Coastal Overview
Notes: Here is a video showing the formation of Louisiana and its coast.

## Slide 12: WHAT CHANGED?
Coastal Overview
of
1927
The Great Mississippi Flood
Notes: As Louisiana’s population grew, the flooding became more problematic. In 1927, the Great Mississippi Flood was the most destructive river flood in U.S. history. Depths reached as much as 30 feet in some places, 16 million acres of land were inundated, and hundreds of thousands of people were displaced.

## Slide 13: BUILDING NEW LEVEES
Army Corps of Engineers built new levees and improved existing ones
Coastal Overview
Flood Control Act of 1928
Notes: In response, the U.S. Army Corps of Engineers was tasked with building levees to higher standards, and improving existing levees. What did this mean? Reduced flooding.

## Slide 14: IMPACT OF LEVEES
Coastal Overview
NOW
Levees led to decreased flooding
Decreased flooding = less sediment deposited
Notes: No flooding means sediment is not getting deposited, and freshwater is not getting delivered to the wetlands that need it.

## Slide 15: OTHER CAUSES OF LAND LOSS
LEVEES
SEA LEVEL RISE
SUBSIDENCE
OIL SPILLS
OIL AND GAS INFRASTRUCTURE
PIPELINE CANALS
STORMS
Coastal Overview
Notes: There are many other factors that contribute to land loss, both naturally occurring and caused by humans.

## Slide 16: COASTAL FEATURE LEGEND
Barrier Islands & Beaches
Wetlands (Marshes and Swamps)
Coastal Ridges
Coastal Projects
Notes: Here are a few of the coastal features we’ll be talking about. I’ll show you some examples in the coming slides.

## Slide 17: BARRIER ISLANDS & BEACHES
Parallel to mainland coast
First speed bump
Provides essential and critical habitat
Reduces wave energy
Coastal Projects
Notes: Barrier islands are one of our first lines of defense. In this photo, you can see waves from the gulf on the left hitting the shore, while the water to the right is calm. Barrier islands reduce wave energy and protect our coast from erosion.

## Slide 18: COASTAL RIDGES
Serves as a natural levee
Impedes overland flow
Naturally elevated above marsh surface
Typically populated with trees
Reduces shoreline erosion
Coastal Projects
Notes: Ridges naturally form along the edges of marshes. They reduce erosion and serve as a natural levee.

## Slide 19: WETLANDS
\
SWAMP
MARSH
Supports woody growth
Primarily grasses and reeds
Flood protection
Fisheries
Habitat
Improved Water Quality
Coastal Projects
Notes: Wetlands act as a “sponge” protecting our shores, reducing wave energy and protecting us from storm surge. Additionally, swamps and marshes serve as vital habitat to many species.

## Slide 20: COASTAL PROJECT TYPES
Freshwater Diversion
Shoreline Protection / Living Shorelines
Barrier Island Restoration
Wetland Protection
Coastal Ridge Restoration
Coastal Projects
Notes: Here are some of the different project types taking place in Jefferson Parish. Next, we will go over some examples of these projects.

## Slide 21: CHRISTMAS TREE RECYCLING PROJECT
Operating since 1991
Reduced erosion rates
Coastal Projects
4 ft/yr vs. 16 ft/yr

## Slide 22: QUESTIONS?
Thank you!